# Fabrication Simulation of 3D C-MEMS/NEMS for Biological Sensing and Manipulation

### 论文摘要

微纳制造技术作为微纳结构和器件的重要制造工具,近年来随着微纳技术的发展和新材料的不断涌现得到了快速的发展。体硅加工技术的发展造就了微纳机电系统（MEM/NEMS）的出现和广泛应用。最近,基于碳微纳加工技术的发展,出现了碳基微纳机电系统（C-MEM/NEMS）. C-MEMS/NEMS技术是将高分子前驱体的微纳图形隔绝空气条件下高温碳化的技术。通过融合光刻技术和高温热解技术,各种碳微纳结构的图形能够很容易的制备。该技术不仅具有大批量低成本的优势,还在应用碳材料的生物兼容性和多样性等方面具有优势,对新型器件的开发具有广阔的前景。但是,国内外在该领域的制备技术和应用研究还处于起步阶段。为此,本论文将开展微纳加工技术,尤其是碳微纳制造技术的研究,并基于碳材料独特的三维结构进行新型器件开发的应用研究。在本论文中,首先,对MEMS, NEMS和C-MEMS/NEMS的研究背景进行了系统和全面的综述。然后,对硅基高深宽比微结构的表面干法刻蚀工艺过程进行了基于刻蚀流的建模分析和仿真；对碳基三维微电极阵列结构的多层制备工艺过程和结构生成原理进行了实验分析；对碳基三维电极阵列结构在生物颗粒操纵和传感中的应用进行了系统分析和建模。最后面向微纳颗粒的介电泳操纵的应用,建立了电场模型,颗粒受力模型,颗粒运动和操纵模型,并对电极结构的设计进行了优化分析。这些分析和应用将为C-MEMS/NEMS的介电泳操纵应用提供设计指导,尤其对大批量和高效的微纳颗粒操纵和碳微纳结构的集成应用具有非常重要的意义。本研究论文在高深宽比微纳结构的加工过程的模拟仿真和开发新型三维微纳结构器件原型方面具有实质性的创新突破。但由于研究时间的关系,大量的后续工作还需要进一步进行,包括建模和仿真的实验应用,加上工艺过程的优化控制及器件原型的完善和集成应用等。

### 论文目录

- 摘要

- Abstract

- 1 INTRODUCTION AND LITERATURE REVIEW OF MEMS/) NEMS AND C-ME MS/NEMS FABRICATION

- 1.1 Project Financial Support

- 1.2 Electromechanical Systems Evaluation

- 1.3 Conventional Micro-Fabrication Approaches

- 1.4 Novel Microfabrication Techniques and Supplies（C-MEMS）

- 1.5 Important Role of Carbonized Photoresist Shrinkage and Electrical Properties in C-MEMS

- 1.6 C-MEMS Prologue

- 1.7 Stimulus Advances

- 1.8 C-NEMS Technology and Miniaturization Impact

- 1.9 C-MEMS/NEMS Biological Aspects

- 1.10 Recent Nanotechnology Applications in Cancer Detection

- 1.11 Conclusion

- 2 FLUX BASED FABRICATION OF SILICON DEEP TRENCH STRUCTURES FOR MEMS

- 2.1 Introduction

- 2.2 Process Modeling

- 2.3 Surface Flux Distribution Models

- 2.4 Simulation Results and Discussion

- 2.5 Conclusion

- 3 MULTI-LAYER C-MEMS/NEMS FABRICATION PROCESS

- 3.1 Literature Review

- 3.2 Processes and Materials

- 3.3 Fabrication Procedure

- 3.4 Multilayer SU-8 Structures Growth

- 3.5 Fabricated C-MEMS Multilayered Structural Applications

- 3.6 Discussion

- 3.7 Conclusion

- 4 DESIGN AND FABRICATION OF DEP-BASED C-MEMS FOR MANIPULATION OF BIOPARTICLES

- 4.1 Introduction and Literature Review

- 4.2 Author Majn Objective

- 4.3 Modeling of 3D Dielectrophresis

- 4.4 DEP-Modelingfor Multishape Microelectrodes Array

- 4.5 Design of 3D Carbon Circular Microelectrode Array

- 4.6 Design of 3D Carbon Multi-shaped Microelectrode Array

- 4.7 Conclusion

- 5 OPTIMIZATION OF DEP-BASED C-MEMS/NEMS STRUCTURES

- 5.1 Results and Discussions Based on Circular Column Microelectrode Array

- 5.2 Results and Discussions Based on Square Column Microelectrode Array

- 5.3 Combined Simulation Analysis of 3D Carbon Circular,Square （90° Edge）,and Triangular（Flat/Sharp）Extruded Microelectrode Array Designs

- 5.4 Process Development of Carbon-MEMS/NEMS

- 5.5 Conclusion

- 6 SUMMARY AND CONCLUSION

- Acknowledgments

- References

- PUBLICATIONS

### 相关论文文献

- [1].“ IEEE-NEMS 2016 The 11~(th) Annual IEEE International Conference on Nano/Micro Engineered and Molecular Systems”通知（英文）[J]. 太赫兹科学与电子信息学报 2015(03)

- [2].IEEE-NEMS2014 THE 9TH IEEE INTERNATIONAL CONFERENCE ON NANO/MICRO ENGINEERED AND MOLECULAR SYSTEMS[J]. 太赫兹科学与电子信息学报 2013(05)

- [3].基于专利分析的NEMS传感器技术发展现状与趋势[J]. 科技促进发展 2019(08)

- [4].IEEE-NEMS2014THE 9TH IEEE INTERNATIONAL CONFERENCE ON NANO/MICRO ENGINEERED AND MOLECULAR SYSTEMS[J]. 太赫兹科学与电子信息学报 2014(01)

- [5].IEEE-NEMS2014 The 9TH IEEE International Conference on Nano/Micro Engineered and Molecular Systems[J]. 太赫兹科学与电子信息学报 2013(04)

- [6].面向NEMS器件的碳纳米管与金属电极电接触研究[J]. 功能材料与器件学报 2012(05)

- [7].IEEE-NEMS系列会议[J]. 太赫兹科学与电子信息学报 2018(05)

- [8].基于静电驱动NEMS混频器结构设计与分析[J]. 传感技术学报 2008(04)

- [9].基于NEMS网络综合实验的教学改进[J]. 纺织教育 2011(04)

- [10].IEEE-NEMS 2017 The 12~(th) Annual IEEE International Conference on Nano/Micro Engineered and Molecular Systems[J]. 太赫兹科学与电子信息学报 2017(01)

- [11].IEEE-NEMS 2019 The 14th Annual IEEE International Conference on Nano/Micro Engineered and Molecular Systems[J]. 太赫兹科学与电子信息学报 2018(05)

- [12].IEEE-NEMS 2019 The 14th Annual IEEE International Conference on Nano/Micro Engineered and Molecular Systems[J]. 太赫兹科学与电子信息学报 2019(01)

- [13].Effect of temperature on pull-in voltage and nonlinear vibration behavior of nanoplate-based NEMS under hydrostatic and electrostatic actuations[J]. Acta Mechanica Solida Sinica 2017(02)

- [14].基于薄层SOI材料的NEMS结构制备技术[J]. 微纳电子技术 2009(05)

- [15].电子信息[J]. 军民两用技术与产品 2017(05)

- [16].基于B/S架构的NEMS网络实验室应用[J]. 实验室研究与探索 2011(04)

- [17].一种B/S架构下基于NEMS的网络实验室教学辅助系统[J]. 价值工程 2014(02)

- [18].迄今最小NEMS加速度传感器问世[J]. 传感器世界 2019(09)

- [19].微纳米分子系统研究领域的最新进展——IEEE NEMS 2013国际会议综述[J]. 太赫兹科学与电子信息学报 2013(03)

- [20].NEMS外场驱动微电机研究进展[J]. 微特电机 2019(03)

- [21].NEMS矢量水听器的海上实验研究[J]. 舰船科学技术 2013(08)

- [22].ELECTRIC FIELD EFFECTS ON YOUNG'S MOLULUS OF NANOWIRES[J]. Acta Mechanica Solida Sinica 2009(06)

- [23].Pull-in instability analyses for NEMS actuators with quartic shape approximation[J]. Applied Mathematics and Mechanics(English Edition) 2016(03)

- [24].Virtual Reality Toolkit for the Assembly of Nanotube-based Nano-electro-mechanical Systems[J]. Chinese Journal of Mechanical Engineering 2011(01)

- [25].微纳米分子系统研究领域的最新进展——IEEE NEMS 2011国际会议综述[J]. 信息与电子工程 2011(02)

- [26].NEMS智能安防监控系统在码头电站管理中的应用[J]. 电工技术 2013(10)

- [27].微纳米分子系统研究领域的最新进展——IEEE NEMS 2014国际会议综述[J]. 太赫兹科学与电子信息学报 2014(03)

- [28].蓬勃发展的跨国公司非实体模式(NEMs)国际化生产[J]. 上海经济 2011(12)

- [29].考虑卡西米尔力的静电激励NEMS吸合特性及其尺寸效应研究[J]. 固体力学学报 2016(03)

- [30].实施国家基本药物制度前后汕头市潮南区基层医疗卫生机构临床用药情况调查[J]. 中国药房 2013(28)

本文来源: https://www.lw50.cn/article/26d49b59dc784ed81fb1d907.html