# PTC太阳能加热装置在沼气工程的应用研究

### 论文摘要

在中中北方,如果没有合适加热设备的沼气装置往往无法实现全年连续产气,尤其是在冬季,没有加热设备的沼气装置将不能稳定,高效产气。此外,沼气装置的加热设备还必须便宜、可靠、对环境无害、能产生较高温度以及高效,使用可再生能源作为沼气装置的外加热源可以满足上述条件,这正是本文研究的内容。咸阳地区直射及散射的太阳辐射量显示,在该地区可以使用太阳能加热沼气装置以提高其发酵温度。沼气装置内外温度的关系是决定加热设备设计的一个重要的因素,根据第二章所述,沼气装置内部的温度对沼气产量影响很大,当装置内温度下降时,沼气产量也下降。在第四章中,使用energy plus这一能量模拟软件结合气象资料对沼气装置的加热进行了8760小时的模拟。第四章分为两部分,第一部分是对两个位于地上的沼气装置的模拟,其中一个沼气装置有加热设备而另一个没有。第四章的第二部分是对于两个位于地下的沼气装置的模拟,一个使用温室结合太阳能的加热装置,另一个没有加热装置。结果表明,使用温室结合太阳能加热的效果好于其他三个,但是这一加热系统并不能达到最理想的温度,所以我们改进了这一装置,使用聚光型太阳能进行加热。与使用两个真空管相比,使用一个放置于抛物面焦线上的真空管的聚光型太阳能效率较低,这主要是因为太阳高度角的变化较大,所以正如第三章所述的那样,使用两个真空管能够产生更多的热量。在第五章中,一个位于地下的沼气装置被作为研究主体,该沼气装置体积为100 m3,位于陕陕省润镇中学校园内。该装置使用人粪尿作为发酵原料,并且每日进料。润镇地区一月份平均-1.6 oC,最低气温-15 oC,该地区平均太阳辐射量为4.5 kwh/m2。本研究的目的就是研究使用聚光型太阳能增进沼气生产的可行性。润镇中学使用的系统包括温室以及聚光型太阳能加热装置,两者结合使得沼气装置达到合适的温度。聚光型太阳能用来加热沼气装置及教室。该使用聚光型太阳能的加热装置可以保证全年沼气生产正常。当气温突然下降,控制单元将使得外加热源开始工作,补充反应装置所需的热量,以保证正常的温度。在冬季,聚光型太阳能系统使得沼气产量增加到每天12 m3,所产沼气输送到学校厨房用作炊事之用。润镇中学聚光型太阳能总的效益为16104元,为60间教室供暖,并且减少CO2排放788.950 1075.830吨。使用温室以及聚光型太阳能加热是十分合适的加热方式,故推荐利用太阳能加热促进沼气生产。此外,温室内部的剩余空间可以用来种植。未来的加热系统将使用聚光型太阳能以及双面温室,新的设计将使得沼气装置内部温度以及沼气产量更高。

### 论文目录

- 摘要

- ABSTRACT

- CHAPTER 1: GENERAL INTRODUCTION

- 1.1. Fossil fuel and renewable energy

- 1.1.1. Fossil fuel

- 1.1.2. Renewable energy

- 1.2. Global energy gap

- 1.3. Effect on environment

- 1.4. Biogas

- 1.4.1. Temperature

- 1.4.2. pH value

- 1.4.3. Percentage of solids

- 1.5. Solar energy

- 1.5.1. Flat solar heater

- 1.5.2. Solar collector

- 1.6. Using solar energy for heating biogas digester

- 1.7. Preface of study

- 1.8. Some software used in study

- 1.8.1. AutoCAD

- 1.8.2. SketchUp

- 1.8.3. MATLAB

- 1.8.4. EnergyPluse

- 1.8.5. Openstudio Plug-in

- 1.9. Innovation

- CHAPTER 2: PROBLEMS STATEMENT: EFFECT OF CHANGING AMBIENT TEMPERATURE DIRECTION ON BIOGAS PRODUCTION

- 2.1. Introduction

- 2.2. Material and methods

- 2.2.1. The experiment design and unit setup with measurement tools

- 2.2.2. Biogas digesters

- 2.2.3. The fermentation material and inoculants

- 2.2.4. Gas production

- 2.2.5. Temperature measurement

- 2.3. Result and Discussion

- 2.3.1. The relation between ambient temperature and the temperature inside the digesters

- 2.3.2. The relation between the temperature inside the digesters and gas production

- 2.3.3. The relation between the temperature inside the digesters and gas production in outdoor group

- 2.3.4. The relation between the temperature inside the digesters and gas production in control room group

- 2.3.5. Comparisons between the gas productions with different Ts in the two groups

- 2.4. Conclusion and summary

- CHAPTER 3: DESIGN AND NUMERICAL SIMULATION OF PARABOLIC TROUGH SOLAR COLLECTOR （PTC） FOR IMPROVE THE EFFICIENCY

- 3.1. Introduction

- 3.2. Design of PTC

- 3.2.1. Focal point and Parabola design

- 3.2.1.1. Focal point

- 3.2.1.2. Frame Design

- 3.2.2. Heating pipe

- 3.2.3. The surface area of solar collector

- 3.3. Solar energy calculation

- 3.3.1. The solar energy flux incident on a tilted surface per day

- 3.3.1.1. Extraterrestrial radiation on a horizontal surface outside earth's atmosphere （Ho）

- 3.3.1.2. Total solar radiation flux incident on horizontal surface of the ground （H）

- 3.3.1.3. Ratio of monthly average radiation on a horizontal surface to the monthly average daily extraterrestrial radiation （kt）

- 3.3.1.4. Beam and diffuse components of daily radiation.

- 3.3.1.5. Total solar radiation flux incident on a fixed slope surface（Ht）

- 3.3.2. The solar energy flux incident on a tilted surface per Hour

- 3.3.2.1. The clear sky beam radiation on a horizontal surface （Icb）

- 3.3.2.2. The clear sky diffuses radiation on a horizontal surface （Icd）

- 3.3.2.3. The clear sky total radiation on a horizontal surface（Ic）

- 3.3.2.4. An hour clearness index（kt ）

- 3.3.2.5. Beam and diffuse components of radiation per hour

- 3.3.2.6. Total radiation on tilted surface（IT）

- 3.4. Conclusion

- CHAPTER 4: SIMULATION OF SOLAR HEATING BIOGAS DIGESTERS ABOVE AND UNDER-GROUND FOR RAISING ORGANIC MATTER TEMPERATURE WITHOUT USING PTC

- 4.1. Introduction

- 4.2. Material and methods

- 4.2.1. Biogas digester above ground

- 4.2.1.1. Design of biogas digester above the ground

- 4.2.1.2. Design of Solar heating system for biogas digester above ground

- 4.2.2. Biogas digester underground

- 4.2.2.1. Design of biogas digester underground

- 4.2.2.2. Design of greenhouse

- 4.2.2.3. Design of inlet

- 4.3. Result and Discussion

- 4.3.1. Environmental variables

- 4.3.2. Biogas digester above ground （D1）

- 4.3.3. Biogas digester above ground with heating system （D2）

- 4.3.3.1. Biogas digester

- 4.3.3.2. Heating system of Biogas digester above ground

- 4.3.4. Biogas digester underground（D3）

- 4.3.5. Biogas digester underground with inlet heating （D4）

- 4.3.5.1. Biogas digester

- 4.3.5.2. Inlet

- 4.3.5.3. Greenhouse

- 4.3.6. Comparison between four digesters

- 4.4. Conclusion

- CHAPTER 5: HEATING BIOGAS DIGESTER BY USING PTC AND GREEN HOUSE

- 5.1. Introduction

- 5.2. Material and methods

- 5.2.1. Description of first part

- 5.2.1.1. Biogas digester

- 5.2.1.2. Solar heating system

- 5.2.1.3. Greenhouse

- 5.2.1.4. Design of hot water auxiliary

- 5.2.1.5. Control unit

- 5.2.2. Description of second part （Future design）

- 5.2.2.1. Biogas digester

- 5.2.2.2. Solar water heater

- 5.2.2.3. The green house

- 5.3. Result and Discussion

- 5.3.1. Green house

- 5.3.2. Solar water heater

- 5.3.3. Biogas digester

- 5.3.4. The new system

- 5.4. Analyze of system and economic study

- 5.4.1. Calculation of total energy for heating and Co2 emissions

- 5.4.2. The overall energy collected by the system

- 5.4.3. Economic study

- 5.5. Conclusion

- CHAPTER 6: CONCLUSION AND RECOMMENDATION

- REFERENCES

- LIST OF TABLE

- LIST OF FIGURES

- APPENDIX A

- APPENDIX B

- ACKNOWLEDGEMENT

- CURRICULUM VITAE

### 相关论文文献

- [1].电动汽车PTC加热器控制改进[J]. 汽车电器 2019(12)

- [2].ERCP与PTC两种胆道支架置入术治疗恶性梗阻性黄疸的疗效对比[J]. 江西医药 2019(12)

- [3].PTC陶瓷加热器替代普通加热器在牙轮钻机上的使用方案[J]. 技术与市场 2020(01)

- [4].PTC温控技术在无源丰度检测装置中的应用[J]. 仪器仪表用户 2020(10)

- [5].美国PTC列控系统研究[J]. 铁道通信信号 2016(11)

- [6].功能性颈淋巴结清扫术在分化型甲状腺癌(PTC)中的应用[J]. 世界最新医学信息文摘 2016(49)

- [7].压敏电阻与PTC热敏电阻配合使用[J]. 电源世界 2015(01)

- [8].PTC热敏电阻在通信设备上的应用研究[J]. 机电信息 2013(33)

- [9].二维及彩色多普勒超声对PTC的诊断探究[J]. 影像研究与医学应用 2018(19)

- [10].MRCP与PTC对胆道梗阻疾病的对比研究[J]. 中国社区医师(医学专业) 2010(26)

- [11].水性石墨烯/碳纳米管/炭黑PTC电热涂料的制备[J]. 广州化学 2020(05)

- [12].医学遗传学教学中PTC尝味实验改革初探[J]. 保健医学研究与实践 2017(01)

- [13].PTC培训模式在急诊护士急救技能培训中的应用[J]. 河南医学研究 2016(04)

- [14].PTC教学模式在急救技能教学中的应用和探讨[J]. 中国高等医学教育 2014(12)

- [15].PTC教学模式在急救护理技术操作中的应用[J]. 广西教育 2015(18)

- [16].手术联合~（131）I、甲状腺片治疗甲状腺乳头状癌(PTC)临床体会[J]. 河南外科学杂志 2014(01)

- [17].跟踪与装配误差对PTC截断因子的影响分析[J]. 可再生能源 2016(02)

- [18].PTC模式在急诊低年资护士应急能力培训中的应用[J]. 齐鲁护理杂志 2014(18)

- [19].基于PTC陶瓷电阻大容量蓄电池组放电车的故障分析和改进[J]. 船电技术 2011(10)

- [20].胃癌组织中Ptc蛋白的表达变化及意义[J]. 山东医药 2010(06)

- [21].陶瓷PTC辅助电加热器在风管机中的应用[J]. 制冷与空调 2010(03)

- [22].基于PTC陶瓷电阻的大容量蓄电池组恒流放电[J]. 蓄电池 2009(03)

- [23].有机载体挥发特性对PTC陶瓷铝电极性能的影响[J]. 电子元件与材料 2010(08)

- [24].石墨/聚乙烯导电复合材料PTC效应稳定性的研究[J]. 塑料工业 2012(S1)

- [25].过氧化钛配合物(PTC)体系在柔性染料敏化太阳能电池中的应用[J]. 影像科学与光化学 2009(06)

- [26].PTC对胰胆管合流异常的诊断[J]. 世界华人消化杂志 2008(09)

- [27].陶瓷PTC电磁继电器分时控制技术研究[J]. 电器 2013(S1)

- [28].高密度聚乙烯/炭纤维复合体系的PTC效应[J]. 高分子材料科学与工程 2011(02)

- [29].ERCP联合PTC治疗ERCP难治性胆道梗阻15例[J]. 中南医学科学杂志 2011(04)

- [30].Ptc展 宁波市鄞州通力液压电器厂[J]. 机床与液压 2018(23)

本文来源: https://www.lw50.cn/article/4e2c4d61a33f1b2b39ca9834.html