# 磁场对乳液法合成聚苯胺取向结构及性能的影响与表征

### 论文摘要

导电聚苯胺（Polyaniline,PANI）作为一种新型的功能高分子材料,越来越受到科学家们的关注。这不仅是因为它具有合成方法简单、掺杂机制独特、环境稳定性良好等优点,而且它还具有广阔的开发与应用前景。但是聚苯胺的难溶解、难熔融、不易加工等特性阻碍了聚苯胺的实用化进程。磁场效应对自由基类的高分子合成具有显著的影响。而磁流体的动力学效应会导致质量传递增强,影响聚合反应的速率及进程。同时,由于聚苯胺分子具有各向异性抗磁磁化率,可导致其内部结构单元在磁场作用下优先沿某一特定方向的生长排列,即发生一定程度的取向,使产物的分子链排列更加有序,结构更加规整,同时表现为材料在物理性能方面的各向异性。磁场可通过影响PANI的微观结构,如共轭链长、分子链规整度、聚集态等,进而对的其宏观性能构成影响,比如:会使PANI的电导率、溶解/分散性、热解温度等产生不同程度的提高。本文在（0.4T）磁场环境和无磁场环境下（其它实验条件相同）,采用乳液聚合法制备了PANI,并通过透射电镜、原子力显微镜、渗透凝胶色谱、傅立叶红外光谱、X-射线衍射、四探针电导率、激光粒度分析、热失重分析、塔菲尔曲线、产物复合膜电阻率的各向异性,以及产物间甲酚溶液的电导率在外电场作用下变化的分析与表征,对比研究了磁场作用对苯胺乳液聚合行为、产物取向结构及性能的影响机制,并通过创新的方法成功地对PANI的取向结构行进了表征。研究结果表明:与无磁场作用下苯胺的乳液聚合相比,磁场作用下苯胺乳液聚合的反应速率加快、产率增加,所得产物的分子量、电导率、溶解/分散性、防腐性、热稳定性及结晶性等也均有提高;磁场作用对乳液聚合法制备PANI的基本单元结构无明显影响,但由于磁场作用下制备的PANI具有更显著的抗磁磁化率的各向异性,即不同方向上粒子对磁场的响应特性发生了明显的分化,极大的增强了微粒间聚集时的取向排列,因此与无磁场作用下制备PANI相比,磁场作用下制备的PANI具有明显的微观取向结构,其微粒有序排列和堆砌成了许多具有一定长/径比的条状聚集体,且在外磁场作用下这种微观的取向排列方式会进一步演变成宏观的取向,随之表现出物理性能上的各向异性。当乳化剂与苯胺摩尔比为0.5,氧化剂与苯胺摩尔比为0.8,pH值为2.53,反应时间为4h时,磁场作用对苯胺乳液聚合行为及产物结构、性能的影响显著,（0.4T）磁场环境下制备PANI的取向程度较高,各主要结构、性能指标较优,且普遍比无磁场环境下制备PANI的好。

### 论文目录

- 摘要

- ABSTRACT

- 1 绪论

- 1.1 课题的研究背景

- 1.2 聚苯胺的结构

- 1.2.1 聚苯胺的分子结构

- 1.2.2 聚苯胺的远程结构

- 1.2.3 聚苯胺的聚集态结构

- 1.3 聚苯胺的导电机理

- 1.3.1 导电机理

- 1.3.2 Mott 变程跳跃模型

- 1.4 聚苯胺的合成

- 1.4.1 聚苯胺聚合机理

- 1.4.2 聚苯胺的合成方法

- 1.5 聚苯胺的应用

- 1.5.1 导电材料

- 1.5.2 防腐涂料

- 1.5.3 传感器

- 1.5.4 隐身材料

- 1.5.5 能源材料

- 1.5.6 智能窗

- 1.5.7 聚苯胺磁性能的应用

- 1.6 磁场对自由基聚合的影响机制

- 1.6.1 磁化学概述

- 1.6.2 自由基对理论

- 1.7 磁场在聚苯胺制备中的应用

- 1.7.1 磁场对苯胺聚合行为的影响

- 1.7.2 磁场对聚苯胺结构的影响

- 1.7.3 磁场对聚苯胺性能的影响

- 1.8 本论文的目的意义及主要研究内容

- 1.8.1 目的意义

- 1.8.2 本课题主要研究内容

- 2 实验部分

- 2.1 主要原料

- 2.2 主要仪器设备

- 2.3 实验装置简图

- 2.4 实验方法

- 2.4.1 乳化剂的选择

- 2.4.2 乳液法制备掺杂聚苯胺

- 2.4.3 PANI/间甲酚（m-cresol）溶液的制备

- 2.4.4 PANI/PVA 分散液的配制

- 2.4.5 钢基材PANI/PVA 膜扳的制备

- 2.4.6 玻璃基材PANI/PVA 复合膜的制备与磁化

- 2.5 性能测试与表征方法

- 2.5.1 产率的测定

- 2.5.2 四探针电导率的测定

- 2.5.3 特性粘度的测定

- 2.5.4 溶解性

- 2.5.5 Tafel 曲线的测定

- 2.5.6 PANI/m-cresol 溶液电导率—温度曲线

- 2.5.7 PANI/PVA 复合膜导电性能各向异性的测定

- 2.5.8 凝胶渗透色谱（GPC）

- 2.5.9 粒度的测定

- 2.5.10 红外光谱分析（FT-IR）

- 2.5.11 X 射线衍射分析（XRD）

- 2.5.12 热重分析（TGA）

- 2.5.13 透射电子显微镜测试（TEM）

- 2.5.14 原子力显微镜分析（AFM）

- 3 结果与讨论

- 3.1 磁场对苯胺乳液聚合行为的影响研究

- 3.1.1 磁场环境下反应时间对聚合行为的影响

- 3.1.2 磁场环境下乳化剂用量对聚合行为的影响

- 3.1.3 磁场环境下氧化剂用量对聚合行为的影响

- 3.1.4 磁场环境下pH 对聚合行为的影响

- 3.2 磁场作用对乳液聚合制备聚苯胺结构的影响

- 3.2.1 取向结构的表征及磁场对PANI 聚集态结构的影响

- 3.2.2 磁场对PANI 链结构的影响

- 3.3 磁场对聚苯胺性能影响的研究

- 3.3.1 四探针电导率分析

- 3.3.2 Tafel 曲线分析

- 3.3.3 TGA 分析

- 3.3.4 溶解率分析

- 4 结论与展望

- 4.1 结论

- 4.2 展望

- 致谢

- 参考文献

- 附录

### 相关论文文献

- [1].ZnO@MOF@PANI core-shell nanoarrays on carbon cloth for high-performance supercapacitor electrodes[J]. Journal of Energy Chemistry 2019(08)

- [2].Thermal conductivity of PVDF/PANI-nanofiber composite membrane aligned in an electric field[J]. Chinese Journal of Chemical Engineering 2018(05)

- [3].Thermal Characteristics of PVA-PANI-ZnS Nanocomposite Film Synthesized by Gamma Irradiation Method[J]. Chinese Physics Letters 2018(11)

- [4].Synthesis and Enhanced Electrochemical Activity of Ag-Pt Bimetallic Nanoparticles Decorated MWCNTs/PANI Nanocomposites[J]. Journal of Wuhan University of Technology(Materials Science) 2018(05)

- [5].Immobilization of PANI on Mesoporous Carbon:Preparation and Supercapacitor Performance[J]. Transactions of Nanjing University of Aeronautics and Astronautics 2018(04)

- [6].A Self-Powered Breath Analyzer Based on PANI/PVDF Piezo-Gas-Sensing Arrays for Potential Diagnostics Application[J]. Nano-Micro Letters 2018(04)

- [7].NiCo_2O_4 decorated PANI–CNTs composites as supercapacitive electrode materials[J]. Journal of Energy Chemistry 2017(01)

- [8].Electrical Conductivity and pH Sensitivity of Ordered Porous Gel Acrylate Polymer Membrane with Nano-PANI Doping[J]. Journal of Harbin Institute of Technology 2017(02)

- [9].接枝聚合法制备PANI/CeO_2-APTMS复合材料及其电化学性能[J]. 高分子材料科学与工程 2017(07)

- [10].花状CuS/PANI复合材料的制备及其电磁屏蔽性能研究[J]. 现代化工 2017(11)

- [11].MnFe_2O_4@PANI@Ag Heterogeneous Nanocatalyst for Degradation of Industrial Aqueous Organic Pollutants[J]. Journal of Materials Science & Technology 2016(02)

- [12].PANI导电水凝胶的制备及其进展[J]. 高分子通报 2020(06)

- [13].原位聚合法制备PANI/RGO导电复合材料的性能[J]. 工程塑料应用 2018(03)

- [14].硅烷偶联剂预处理PANI对水性涂料性能的影响[J]. 精细化工 2017(11)

- [15].Synthesis and supercapacitor characteristics of PANI/CNTs composites[J]. Chinese Science Bulletin 2010(11)

- [16].Preparation of Surfactants Directed PANI/In_2O_3 Nanocomposite Thin Films and Its NH_3-Sensing Properties[J]. Journal of Electronic Science and Technology 2010(02)

- [17].Preparation,Characterization and Comparative NH_3-sensing Characteristic Studies of PANI/inorganic Oxides Nanocomposite Thin Films[J]. Journal of Materials Science & Technology 2010(07)

- [18].Chlorine gas sensors using hybrid organic semiconductors of PANI/ZnPcCl_(16)[J]. 半导体学报 2010(08)

- [19].Investigation of Novel Short Fiber-like Polyaniline/Cerium Nitrate Composite[J]. Journal of Wuhan University of Technology(Materials Science) 2019(01)

- [20].Nano-Au@PANI蛋黄空心结构电极材料的构筑及超级电容性能[J]. 材料导报 2018(01)

- [21].PANI/MoS_2复合材料的制备及其电化学性能研究[J]. 当代化工 2018(05)

- [22].双脉冲电镀制备PbO_2-PANI复合电极的研究[J]. 化工新型材料 2018(07)

- [23].Two-dimensional polyaniline nanosheets via liquid-phase exfoliation[J]. Chinese Physics B 2017(04)

- [24].Preparation and Antibacterial Activity of Three-component NiFe_2O_4@PANI@Ag Nanocomposite[J]. Journal of Materials Science & Technology 2014(07)

- [25].PMOV_2/PANI/TiO_2复合材料的制备及光催化性能[J]. 化工新型材料 2012(12)

- [26].Synthesis and characterization of conducting polyaniline nanocomposites containing ZnO nanorods[J]. Progress in Natural Science:Materials International 2012(04)

- [27].PANI/Fe-杭锦2~#土催化剂对乙酸的光催化降解研究[J]. 内蒙古师范大学学报(自然科学汉文版) 2019(05)

- [28].电场-抽滤法制备VACNTs/PANI复合膜及其热性能研究[J]. 广州化工 2018(15)

- [29].Effect of CNTs and nano ZnO on physical and mechanical properties of polyaniline composites applicable in energy devices[J]. Progress in Natural Science:Materials International 2016(06)

- [30].Ternary Fe_3O_4@PANI@Au nanocomposites as a magnetic catalyst for degradation of organic dyes[J]. Science China(Technological Sciences) 2017(05)

本文来源: https://www.lw50.cn/article/546867d6cd28fbef9e1f6733.html