# 多晶热电材料Seebeck系数的晶粒尺寸效应研究及分段热电偶优化设计

### 论文摘要

热电器件以其无污染、无噪声、无磨损、体积小、安全可靠性高、热-电转化速度快和输出功率范围广等优点,深受广大学者的关注。其中,对热电器件具有重要影响的因素主要包括：热电材料的优值系数（与Seebeck系数、热导率、电导率相关）、器件几何结构、器件的制造工艺和热电器件冷热端的散热形式。那么对以上因素的研究就成了发展热电器件的重要问题。本文采用Boltzmann输运理论和商业有限元软件ANSYS对多晶块材热电材料的Seebeck系数的晶粒尺寸效应和热电器件的结构优化设计作了部分研究,得到了一些有意义的结果。首先,针对多晶块材热电材料Seebeck系数的尺寸效应,从材料的微结构角度考虑电子的晶界散射,通过求解电子的输运方程,建立了多晶块材热电材料的Seebeck系数尺寸效应的理论预测模型。进而研究了多晶块材热电材料的Seebeck系数晶粒尺寸效应,探讨了透射率、温度和平均自由程等对Seebeck系数的影响。结果表明,本文的理论模型能有效预测多晶块材热电材料的Seebeck系数的晶粒尺寸效应,且与相关实验结果具有较好的一致性。透射率、温度以及平均自由程等对Seebeck系数的晶粒尺寸效应也存在明显的影响。其次,针对热电器件的转化效率,利用ANSYS软件从器件的结构设计出发,考虑材料性能参数随温度的变化,建立了分段热电偶的有限元模型。进而分析了负载电阻、热电偶支腿长度、横截面积、分段比例以及接触电阻和接触热阻对于器件转化效率的影响。总之,通过本文对于热电材料Seebeck系数和热电器件的结构优化设计的研究,为热电材料以及器件的发展提供了相应的理论依据和设计手段。

### 论文目录

- 摘要

- Abstract

- 第一章 绪论

- 1.1 热电效应的历史背景及应用

- 1.2 热电效应简介

- 1.3 热电器件的主要用途

- 1.4 热电材料性能参数的理论研究进展

- 1.5 本文的主要工作

- 第二章 多晶热电材料Seebeck系数的晶粒尺寸效应理论研究

- 2.1 纳米材料及其性能参数尺寸效应的研究概述

- 2.2 Boltzmaan输运理论

- 2.3 多晶热电材料的Seebeck系数晶粒尺寸效应的理论模型

- 2.4 计算结果及讨论

- 2.5 本章小结

- 第三章 热电器件的有限元模拟分析

- 3.1 热电器件的研究进展

- 3.2 通用有限元分析软件ANSYS简介

- 3.3 ANSYS分析热电耦合问题简介

- 3.4 热电器件的有限元模拟

- 3.5 小结

- 第四章 结束语

- 参考文献

- 附录 在学期间发表学术论文和科研成果

- 致谢

### 相关论文文献

- [1].The effects of interface scattering on thermoelectric properties of film thermoelectric materials[J]. Chinese Science Bulletin 2014(25)

- [2].Impact of grain size on the Seebeck coefficient of bulk polycrystalline thermoelectric materials[J]. Chinese Science Bulletin 2010(01)

- [3].Bipolar Thermoelectrical Transport of Sn Se Nanoplate in Low Temperature[J]. Chinese Physics Letters 2020(01)

- [4].Seebeck效应的教学体会[J]. 教育教学论坛 2017(14)

- [5].热电材料Seebeck系数测定中的误差分析[J]. 科技风 2014(17)

- [6].Optoelectronic properties and Seebeck coefficient in SnSe thin films[J]. Journal of Semiconductors 2016(09)

- [7].塞贝克系数的估算[J]. 科技创新与应用 2020(02)

- [8].基于Seebeck效应的配电变压器绕组材质无损鉴别装置及测试分析[J]. 电力自动化设备 2019(02)

- [9].碳纤维水泥基复合材料Seebeck效应研究现状[J]. 材料导报 2017(01)

- [10].Experimental studies on overall property of thermoelectric modules with sandwiched structures[J]. Chinese Science Bulletin 2014(Z1)

- [11].钢渣混凝土的Seebeck效应研究[J]. 重庆建筑大学学报 2008(03)

- [12].Thermoelectric properties of LaFe_3CoSb_(12) skutterudite materials with different nanostructures[J]. Journal of Rare Earths 2011(10)

- [13].First principle investigation of the electronic and thermoelectric properties of Mg_2C[J]. Chinese Physics B 2016(02)

- [14].Research on the Seebeck effect in efficient turning process and improving tool life[J]. Journal of Harbin Institute of Technology 2012(06)

- [15].Thermoelectric properties of Bi_(1.5)Pb_(0.5)Sr_(2-x)La_xCo_2O_y polycrystalline materials[J]. Rare Metals 2011(05)

- [16].HPHT synthesis and electrical transport properties of Sm_xCo_4Sb_(12)[J]. Journal of Rare Earths 2010(03)

- [17].原子无序对half-Heusler合金CoCrAl电子结构及Seebeck系数的影响[J]. 武汉科技大学学报 2019(03)

- [18].Thermoelectric transport properties of Bi CuSeO with embedded La0.8Sr_(0.2)CoO_3 nanoinclusions[J]. Science China(Technological Sciences) 2016(07)

- [19].Synthesis and high temperature thermoelectric transport properties of Si-based type-Ⅰ clathrates[J]. Chinese Physics B 2009(07)

- [20].Transport properties of Zintl phase Yb_(1-x)Ca_xCd_2Sb_2 at low temperature[J]. Journal of Rare Earths 2010(03)

- [21].Preparation and Thermoelectric Properties of SiO_2/β-Zn_4Sb_3 Nanocomposite Materials[J]. Journal of Wuhan University of Technology(Materials Science Edition) 2009(05)

- [22].自旋Seebeck效应实验研究进展[J]. 材料导报 2015(05)

- [23].Electrical Properties of GeTe-based Ternary Alloys[J]. Journal of Wuhan University of Technology(Materials Science) 2018(02)

- [24].Recent Progress of Two-Dimensional Thermoelectric Materials[J]. Nano-Micro Letters 2020(03)

- [25].Graphene-enhanced thermoelectric properties of p-type skutterudites[J]. Chinese Physics B 2018(04)

- [26].Electronic structures and thermoelectric properties of solid solutions CuGa_(1-x) In_xTe_2 : A first-principles study[J]. Chinese Physics B 2014(03)

- [27].Anion-site-modulated thermoelectric properties in Ge_2Sb_2Te_5-based compounds[J]. Rare Metals 2020(10)

- [28].Preparation and electronic characteristics of anionic perylene bisimide films[J]. Science China(Chemistry) 2017(10)

- [29].Effect of pressure on electronic and thermoelectric properties of magnesium silicide: A density functional theory study[J]. Chinese Physics B 2016(05)

- [30].Effect of manganese doping on the thermoelectric properties of Zintl phase EuCd_2Sb_2[J]. Journal of Rare Earths 2015(10)

本文来源: https://www.lw50.cn/article/903ef1a94f7d0aaef0559943.html