# 磁控溅射法制备YBCO原子层热电堆薄膜研究

### 论文摘要

YBCO外延地生长在倾斜的SrTiO3衬底上时,YBCO薄膜表面法向与YBCO的c轴成α角,若有激光光沿z轴方向入射YBCO表面时,z轴有激光感生热电电压产生。这种热电材料称为原子层热电材料。这种激光感生热电电压器件(LITV)具有响应快(纳秒到皮秒)、响应光谱宽(光谱范围从紫外到红外)、灵敏度高、非制冷探测、高稳定性、易集成、成本低廉的特点,有很广阔的应用前景。本文就YBCO的制备、薄膜的生长条件、不同条件对薄膜的影响,以及YBCO原子层热电堆进行了研究：1、采用固相法制备YBCO,对不同的烧结温度进行了研究。分别对890℃、900℃、910℃、920℃、930℃温度下制备的YBCO经XRD分析发现,920℃温度下制备的YBCO杂相少,质量最好。2、采用直流磁控溅射法制备了YBCO薄膜,研究了YBCO薄膜生长过程中不同条件对薄膜生长的影响,包括不同总气压、氧氩比、厚度和退火温度,通过XRD分析,当总气压为40Pa、氧氩比为1：2、厚度为1μm、退火温度为800℃时,是薄膜生长的最佳条件。3、以总气压为40Pa、氧氩比为1：2、厚度为1μm、退火温度为800℃为实验条件,在倾斜角为20。的SrTiO3上生长了厚度为1μm的YBCO薄膜,制作成为激光感生热电电压器件,并设计了测量系统进行了测量,结果表明LITV与激光能量成线性关系。

### 论文目录

- 摘要

- Abstract

- 1 概述

- 1.1 YBCO的基本性质

- 1.2 激光感生热电电压发展史

- 1.3 国内外研究现状

- 1.4 论文的主要研究内容

- 2 激光感生热电电压原理

- 2.1 各向异性Seebeck效应

- 2.2 原子层热电堆材料

- 2.3 原子层热电堆模型

- 2.4 包含时间因子的LITV

- 2.5 薄膜参量对感生热电电压的影响

- 3 YBCO靶材的制备和表征

- 3.1 YBCO的制备方法简介

- 3.1.1 固相法

- 3.1.2 液相法

- 3.1.3 气相法

- 3.2 固相法制备YBCO

- 3.2.1 研磨与烧结

- 3.2.2 压片与成型

- 3.3 固相法制备YBCO及工艺研究

- 3.4 YBCO表征方法

- 3.5 实验结果分析

- 4 YBCO薄膜的制备和表征研究

- 4.1 引言

- 4.2 YBCO薄膜的制备方法介绍

- 4.2.1 脉冲激光沉积法（PLD）

- 4.2.2 金属有机物化学气相沉积（MOCVD）

- 4.2.3 金属有机溶液沉积（MOD）

- 4.2.4 溅射法

- 4.3 试验方法

- 4.3.1 直流溅射镀膜法

- 4.4 直流磁控溅射制备YBCO

- 4.4.1 实验装置

- 4.4.2 试验流程

- 4.5 溅射氛围研究

- 4.6 氧分压对YBCO薄膜的影响

- 4.7 厚度对薄膜影响研究

- 4.8 退火温度对薄膜质量的影响

- 4.8.1 退火温度对005峰的影响

- 4.8.2 退火温度对薄膜表面形态的影响

- 5 YBCO原子层热电堆的制作

- 5.1 引言

- 5.2 探头的制作

- 5.2.1 薄膜的制作

- 5.2.2 电极的制作

- 5.2.3 封装

- 5.3 测试实验

- 5.3.1 测量系统设计

- 5.3.2 实验方法

- 5.4 测量结果分析

- 6 结论

- 参考文献

- 致谢

- 个人简历

### 相关论文文献

- [1].一步热处理制备氧化硼掺杂的YBCO超导膜（英文）[J]. 稀有金属材料与工程 2020(05)

- [2].Enhancing superconductivity of ultrathin YBa_2Cu_3O_(7-δ) films by capping non-superconducting oxides[J]. Chinese Physics B 2019(06)

- [3].Thickness modulation effect of CeO_2 layer for YBCO films grown by pulsed laser deposition[J]. Rare Metals 2018(03)

- [4].小型YBCO超导脉冲变压器线圈结构优化设计[J]. 低温物理学报 2016(06)

- [5].YBCO超导层的a轴晶生长研究[J]. 低温物理学报 2017(02)

- [6].Effects of thickness on superconducting properties and structures of Y_2O_3/BZO-doped MOD-YBCO films[J]. Chinese Physics B 2015(05)

- [7].Enhanced superconducting performance in solution-derived YBCO-BaZrO_3composite film[J]. Progress in Natural Science:Materials International 2020(02)

- [8].Temperature-dependent Raman scattering and photoluminescence in YBa_2Cu_3O_7 doped with SiO_2 and Zn_(0.95)Mn_(0.05)O nanoparticles:comparative study[J]. Rare Metals 2019(08)

- [9].新型自润滑YBa_2Cu_3O_7/Cu复合材料的制备及性能[J]. 复合材料学报 2016(02)

- [10].Fe-doped epitaxial YBCO films prepared by chemical solution deposition[J]. Journal of Modern Transportation 2014(01)

- [11].掺杂YBCO超导体系的平均电离势研究[J]. 计算机与应用化学 2014(05)

- [12].Fabrication of YBCO superconducting microarray by sol-gel process using photosensitive metal chelates[J]. Science China(Technological Sciences) 2013(06)

- [13].Effect of humidity on microstructure and properties of YBCO films prepared by Electron Beam Coevaporation[J]. Science China(Technological Sciences) 2012(08)

- [14].YBCO材料的发展及其应用[J]. 江苏陶瓷 2012(04)

- [15].Effect of Y_2Ba_4CuWO_y Addition on the Properties of Single Domain YBCO Superconductors by TSIG Technique[J]. 稀有金属材料与工程 2011(S3)

- [16].Effect of Y_2Ba_4CuNbO_y on the Properties of Single Domain YBCO Superconductor by TSIG Process[J]. 稀有金属材料与工程 2011(S3)

- [17].Preparation of YBCO Coated Conductors on RABiTS Substrate with Advanced TFA-MOD Method[J]. 稀有金属材料与工程 2011(S3)

- [18].Structure and transport studies on nanometer YBCO/PBCGO multilayers[J]. Chinese Science Bulletin 2009(15)

- [19].High Quality YBCO Film Growth on SrTiO_3-Buffered LaAlO_3 Substrate by Full Solution Method[J]. Journal of Materials Science & Technology 2008(06)

- [20].YBCO掺杂效应研究进展[J]. 南昌大学学报(工科版) 2008(04)

- [21].预处理气氛对电子束蒸发制备YBCO薄膜性能和结构的影响[J]. 低温与超导 2013(02)

- [22].金属有机物化学气相法制备YBCO超导薄膜研究[J]. 低温与超导 2010(03)

- [23].Growth orientation and superconducting properties of YBa_2Cu_3O_(7-δ) films prepared by the low-fluorine sol-gel process[J]. 半导体学报 2010(08)

- [24].Effect of humidity on microstructure and properties of YBCO film prepared by TFA-MOD method[J]. Journal of Rare Earths 2009(03)

- [25].Fabrication of YBCO Coated Conductors on Biaxial Textured Metal Substrate by All-Sputtering[J]. Journal of Electronic Science and Technology of China 2008(02)

- [26].正负错配纳米颗粒掺杂对YBCO薄膜性能影响的研究[J]. 无机材料学报 2019(08)

- [27].低阻YBCO超导接头的设计和工艺优化[J]. 低温与超导 2018(02)

- [28].YBCO堆叠高温超导磁体的磁悬浮振动传递特性实验研究[J]. 低温物理学报 2018(03)

- [29].二代YBCO带材接头电学性能低温实验研究[J]. 低温与超导 2017(10)

- [30].热处理气氛中氧含量对YBCO薄膜性能的影响（英文）[J]. 稀有金属材料与工程 2016(10)

本文来源: https://www.lw50.cn/article/b3bec31a18174a394016eb64.html