# 聚（3，4-乙撑二氧噻吩）复合材料的制备及其电化学性质的研究

### 论文摘要

超级电容器因具有比功率高、比电容高、循环性能好、成本低、“绿色”环保等众多优点而广泛应用于航空航天、交通运输、电子计算机等领域。目前,导电聚合物以其快速高效充放电、温度宽、环境友好、成本低的特性,成为一种很有前途的超级电容器电极材料。其中聚3, 4-乙撑二氧噻吩（简称为PEDOT）尤其备受关注,但是PEDOT因其理论比容量低等缺点而被限制发展。因此本文主要研究PEDOT的复合材料来克服其不足,具体内容如下:（1）以碳纳米管（CNTs）为基体,制备不同CNTs质量百分比的PEDOT/CNTs纳米复合物,并探讨其电化学性能。考虑到CNTs分散性和相容性不良,因此对CNTs进行聚苯乙烯磺酸盐（PSS）的修饰,并水热法成功制备出核-壳型PEDOT/PSS-CNTs复合材料,其比电容达198.2 F·g-1,循环2000圈以后比电容衰减26.9%。同时,研究以该复合材料为电极组装成对称电容器来研究其电化学电容行为。（2）由于金属氧化物的能量密度一般都比较高,因此本文采用微波法和界面聚合法分别制备PEDOT/RuO2·xH2O和PEDOT/MnO2纳米复合物。并证明PEDOT/RuO2·xH2O复合物在150 oC热处理后有良好的电化学可逆性和电容特性,而且在0.15 A g-1电流密度下比电容达到153.3 F g-1,当升高到0.8 A g-1时,比容量衰减量大约为17%。另外,制备的PEDOT/MnO2的纳米复合物证明是一种具有多孔孔道结构的无定型材料,当在-0.20.8 V （vs. SCE）范围内,电流密度为0.5 A·g-1时,单电极比容量达到196.3 F·g-1,500次循环后仍保持有90%的比容量。（3）本文制备了PEDOT/PANI纳米复合物,并和活性碳组成混合电容器。该混合电容器在1.0 V的电位窗口下,以0.5 M H2SO4为电解质,当电流密度为1/2 A g-1时,比容量达30.7 F g-1,功率密度达到324.9 W kg-1。为了进一步提高该混合电容器的性能,我们考虑将含有+1价态的无机金属盐与H2SO4溶液组成混合电解液体系,电化学测试表明在0.5 M H2SO4 + 0.2 M K2SO4混合体系下,混合电容器的比电容,能量密度和功率密度具有明显的提高。

### 论文目录

- 摘要

- Abstract

- 第一章 绪论

- 1.1 引言

- 1.2 超级电容器的研究背景及其发展现状

- 1.2.1 超级电容器的结构与特点

- 1.2.2 超级电容器的分类与工作原理

- 1.3 超级电容器电极材料的研究进展

- 1.3.1 碳基电极材料的研究进展

- 1.3.2 金属氧化物电极材料的研究进展

- 1.3.3 导电聚合物电极材料的研究进展

- 1.4 本课题的主要研究内容

- 第二章 导电聚合物聚（3,4-乙撑二氧噻吩）/碳纳米管复合材料的电化学电容行为

- 2.1 聚（3，4-乙撑二氧噻吩）/碳纳米管复合物的制备及其电化学性能

- 2.1.1 引言

- 2.1.2 实验部分

- 2.1.3 结果与讨论

- 2.1.4 小结

- 2.2 聚（3，4-乙撑二氧噻吩）/功能化碳纳米管复合物的制备及电化学性能

- 2.2.1 引言

- 2.2.2 实验部分

- 2.2.3 结果与讨论

- 2.2.4 小结

- 第三章 导电聚合物聚（3,4-乙撑二氧噻吩）/金属氧化物复合材料的电化学性能研究

- 2·XH2O 微波合成及其电化学性能'>3.1 聚（3，4-乙撑二氧噻吩）/ RUO2·XH2O 微波合成及其电化学性能

- 3.1.1 引言

- 3.1.2 实验部分

- 3.1.3 结果与讨论

- 3.1.4 小结

- 3.2 聚（3，4-乙撑二氧噻吩）/二氧化锰的界面聚合及其电化学电容行为

- 3.2.1 引言

- 3.2.2 实验部分

- 3.2.3 结果与讨论

- 3.2.4 小结

- 第四章 导电聚合物聚（3,4-乙撑二氧噻吩）/其他导电聚合物复合材料的电化学性能研究

- 4.1 聚（3,4-乙撑二氧噻吩）/PANI 纳米复合物和活性炭的混合电容器的电化学性能

- 4.1.1 引言

- 4.1.2 实验部分

- 4.1.3 结果与讨论

- 4.1.4 小结

- 4.2 基于 PEDOT/PANI 复合材料和活性炭的混合电容器在酸性混合电解液中电化学性能的研究

- 4.2.1 引言

- 4.2.2 实验部分

- 4.2.3 结果与讨论

- 4.2.4 小结

- 第五章 总结与展望

- 参考文献

- 致谢

- 在学期间的研究成果及发表的学术论文

### 相关论文文献

- [1].PEDOT:PSS对电极的制备及其光电性能研究[J]. 山东化工 2020(05)

- [2].PEDOT: Fundamentals and Its Nanocomposites for Energy Storage[J]. Chinese Journal of Polymer Science 2020(05)

- [3].Optimization of Ethylene Glycol Doped PEDOT:PSS Transparent Electrodes for Flexible Organic Solar Cells by Drop-coating Method[J]. Chinese Journal of Polymer Science 2019(08)

- [4].PEDOT基对电极染料敏化太阳能电池研究进展[J]. 材料导报 2017(07)

- [5].Efficient and Air-Stable Planar Perovskite Solar Cells Formed on Graphene-Oxide-Modified PEDOT:PSS Hole Transport Layer[J]. Nano-Micro Letters 2017(04)

- [6].Transparent and conductive PEDOT:PSS/Ag NW/PEDOT:PSS hybrid films prepared by spin-coating at room temperature[J]. Journal of Semiconductors 2015(12)

- [7].囊泡模板法制备PEDOT空心微球及其对抗坏血酸的电催化氧化性能[J]. 功能高分子学报 2015(04)

- [8].In-situ characterization of electrochromism based on ITO/PEDOT:PSS towards preparation of high performance device[J]. Chinese Physics B 2016(02)

- [9].导电聚合物PEDOT:PSS研究进展[J]. 化工管理 2016(29)

- [10].Preparation of Composited Graphene/PEDOT:PSS Film for Its Possible Application in Graphene-based Organic Solar Cells[J]. Journal of the Chinese Ceramic Society 2015(02)

- [11].石墨烯/PEDOT复合材料的制备及性能研究[J]. 辽宁化工 2015(07)

- [12].Electrosynthesis and Characterization of Aminomethyl Functionalized PEDOT with Electrochromic Property[J]. Chinese Journal of Polymer Science 2015(11)

- [13].Polymer Solar Cells Using a PEDOT:PSS/Cu Nanowires/PEDOT:PSS Multilayer as the Anode Interlayer[J]. Chinese Physics Letters 2015(07)

- [14].PEDOT的电化学合成及其在固态染料敏化太阳能电池中的应用研究[J]. 化学学报 2020(10)

- [15].PEDOT:PSS导电性能优化方法的研究进展[J]. 塑料工业 2016(08)

- [16].Hybrid solar cells constructed of macroporous n-type GaP coated with PEDOT:PSS[J]. Chinese Chemical Letters 2015(04)

- [17].High efficiency bulk heterojunction organic solar cell by using high conductivity modified PEDOT:PSS as a buffer layer[J]. Optoelectronics Letters 2012(05)

- [18].Influence of PEDOT:PSS buffer layer on the performance of organic photocoupler[J]. Optoelectronics Letters 2009(03)

- [19].Tailored PEDOT:PSS hole transport layer for higher performance in perovskite solar cells: Enhancement of electrical and optical properties with improved morphology[J]. Journal of Energy Chemistry 2020(05)

- [20].MoS_2-PEDOT@Ni F复合材料的制备及其电催化析氢性能[J]. 化学研究与应用 2020(07)

- [21].PEDOT/PSS类复合膜的湿敏性能研究[J]. 胶体与聚合物 2018(04)

- [22].Conductivity enhancement of PEDOT:PSS film via sulfonic acid modification: application as transparent electrode for ITO-free polymer solar cells[J]. Science China(Chemistry) 2018(09)

- [23].Analysis on the Characteristic Properties of PEDOT Nano-particle Based on Reversed Micelle Method[J]. Journal of Wuhan University of Technology(Materials Science Edition) 2011(03)

- [24].Synthesis and Structure of PEDOT Prepared through a Modified LB Film Method[J]. 结构化学 2011(11)

- [25].电致变色导电聚合物PEDOT的研究进展[J]. 材料导报 2010(13)

- [26].高导电PEDOT/PSS复合材料改性研究进展[J]. 工程塑料应用 2018(08)

- [27].PEDOT/石墨烯复合材料的制备及其抗静电性能研究[J]. 涂料工业 2017(05)

- [28].Real-time detection of Cu(Ⅱ) with PEDOT:PSS based organic electrochemical transistors[J]. Science China(Chemistry) 2017(09)

- [29].Anticorrosion Performance of Epoxy Coatings Containing Small Amount of Inherently Conducting PEDOT/PSS on Hull Steel in Seawater[J]. Journal of Materials Science & Technology 2013(07)

- [30].小分子甜菜碱改善PEDOT/木质素空穴传输性能[J]. 化工技术与开发 2020(05)

本文来源: https://www.lw50.cn/article/e546ef6e88236e3cc3a564a3.html