# 尼龙6与聚碳酸酯共混体系热学和微观形貌研究及其应用

### 论文摘要

本文对尼龙6与双酚A型聚碳酸酯合金的增容。尼龙6和聚碳酸酯均为重要的工程塑料,二者的性质具有互补的优势。有机溶剂会侵蚀聚碳酸酯,但对尼龙6没有影响;尼龙6具有强吸水性,而聚碳酸酯是憎水的;尼龙6具有低温脆性,而聚碳酸酯在低温下是韧性的。故二者的合金能够综合两种聚合物的优点,具有工程应用的巨大潜力。正因为如此,二者在合金中的相容性一直是人们关注的热点。关于尼龙6与聚碳酸酯的相容性,历来有不同的说法。一些人认为尼龙末端的胺基可与聚碳酸酯末端的羟基可通过反应相连,故二者具有天然的相容性。但在实际工作中发现,仅依赖末端作用不足以造成二者的相容,尤其是当聚合物的分子量较高时。故寻求尼龙6与聚碳酸酯的有效增容剂仍是值得深入探讨的课题。本文选择一种低分子量环氧单体——双酚A型缩水甘油醚(DGEBA)作为增容剂。其末端的环氧基既可以与羟基作用,也可同胺基作用。混入尼龙6与聚碳酸酯的合金后,合金相态显著细化。在PA6/PC=80/20 to20/80w/w组成范围内呈双连续相结构,在两端的组成为海岛结构。由于DGEBA强化了两相间的相互作用,聚碳酸酯的玻璃化温度随尼龙6含量的增加逐步降低。尼龙6的结晶动力学研究表明,结晶速率随聚碳酸酯含量增高而下降。这些现象均表明二者实现了增容化。研究了高度交联丁腈橡胶粉末的马来酸酐化,发现当橡胶粉末/引发剂/马来酸酐质量比为30:1:2时可获得最高的相对接枝率。以这种酸酐化橡胶粉末(MPNBR)为增容剂,研究了尼龙6/聚碳酸酯的增容。加入MPNBR后,合金相态发生改变,不再能观察到双连续相,在全部组成均呈海岛结构,但MPNBR使分散相尺寸显著降低。在热性能上,MPNBR的效果与DGEBA相似,同样观察到尼龙6结晶速率的下降与增容对聚碳酸酯玻璃化温度的影响。表明DGEBA同样是一种有效的增容剂。冲击强度测试再次证实了增容的效果。两种增容剂的任一种加入量为1wt%时,可把合金体系的冲击强度提高近一个数量级,达到工程应用的水平。

### 论文目录

- 摘要

- Abstract

- Chapter One.INTRODUCTION

- 1.1.Introduction

- 1.2.Crystalline-amorphous structures

- 1.3.Polymer Physical Structure

- 1.4.Electrical properties

- 1.5.Polymer Blends

- 1.6.Polymers to classified

- 1.7.Chemical properties of polymers and Polymerization

- 1.8.Polymer characterization and Polymer degradation

- 1.9.Polymeric Transitions

- 1.10.States Of polymers

- 1.11.The difference between a polymer and a plastic

- 1.12.Different between step Polymerization and Chain Polymerization

- Chapter Two.Describe of the polyamifle and polycarbonates

- 2.1.background

- 2.2 Scope of the thesis

- 2.3.polyamides

- 2.4.Polycarbonate

- 2.5.Electrical & Electronics（E&E）

- 2.6.grades available

- 2.7.Epoxy Resins

- Chapter Three.Technology of blending between polyamide6 and polycarbonate.

- 3.1.Background

- 3.2 Brabender

- 3.3.Experimental methods

- Chapter Four.Compatibilization of PA6/PC blendes by Epoxy Resin

- 4.1 introduction

- 4.2.EXPERIMENTAL

- 4.3.Materials

- 4.4.Blends Preparation

- 4.5.Characterization and Measurements

- 4.6 Results and Discussion

- Summary

- Chapter Five.Compatibilization of PA6/PC blendes by butadieneacrylonitrile rubber of PA6/PC blends.

- 5.1.Background

- 5.2.Experimental

- 5.3.Materials

- 5.4.Maleic anhydride grafting of powder rubber

- 5.5.Blends Preparation

- 5.6.Characterization

- 5.7.Results and discussion

- Summary

- Chapter Six.Application Polymer of Solar cells Technologies

- 6.1.Introduction

- 6.2.High efficiency thin film solar cells on flexible polymer sheet

- 6.3.Heterojunction of plastic solar cells

- 6.4.Structure of the organic solar cell

- 6.5.Encapsulation Solar Cells by EVA

- Summary

- Conclusions

- References

- Acknowledgments

- PUBLICATION LIST

- Curriculum vitae

- 北京化工大学博士研究生学位论文答辩委员会决议书

### 相关论文文献

- [1].天辰齐翔百万t尼龙66新材料产业基地开工[J]. 化学推进剂与高分子材料 2020(02)

- [2].尼龙制品吸水性的研究[J]. 汽车实用技术 2020(14)

- [3].尼龙的又一创新——透明电子设备的基础材料[J]. 中国纤检 2020(08)

- [4].高抗冲尼龙畚斗性能浅析[J]. 粮食加工 2020(05)

- [5].尼龙65盐及尼龙65的制备研究进展[J]. 化工新型材料 2020(09)

- [6].河南提速中国尼龙城建设[J]. 合成纤维工业 2019(03)

- [7].尼龙66切片市场分析及前景展望[J]. 中国石油和化工经济分析 2019(07)

- [8].中国尼龙6切片市场分析及前景展望[J]. 中国石油和化工经济分析 2019(07)

- [9].我国尼龙6和尼龙66发展研究[J]. 能源与环保 2018(06)

- [10].电子及汽车用的高热稳定尼龙[J]. 现代塑料加工应用 2016(06)

- [11].特种尼龙的发展及研究综述[J]. 山东化工 2017(02)

- [12].朗盛的2种新型尼龙[J]. 现代塑料加工应用 2017(02)

- [13].兰蒂奇集团推出创新型特殊尼龙系列[J]. 绿色包装 2017(04)

- [14].兰蒂奇集团推出创新型特殊尼龙系列[J]. 乙醛醋酸化工 2017(05)

- [15].尼龙66在工业上的应用及发展前景[J]. 化工管理 2017(15)

- [16].兰蒂奇集团推出创新型特殊尼龙系列[J]. 塑料工业 2017(04)

- [17].奥升德发布尖端汽车行业的尼龙66产品组合[J]. 塑料科技 2017(06)

- [18].高流动性增韧尼龙66材料的研究[J]. 塑料工业 2017(06)

- [19].无机材料玻璃纤维对尼龙66改性的影响[J]. 科技经济市场 2017(06)

- [20].尼龙66生产现状与发展方向预测[J]. 科技与创新 2016(06)

- [21].透明尼龙性能与应用[J]. 西部皮革 2016(08)

- [22].烧结尼龙,聚亚安酯,铁[J]. 美术观察 2016(08)

- [23].尼龙-66市场分析和发展预测[J]. 现代化工 2013(11)

- [24].高流动性尼龙6的制备及表征[J]. 塑料工业 2012(S1)

- [25].相分离法制备尼龙粒子的影响因素研究[J]. 塑料工业 2012(S1)

- [26].尼龙6/尼龙66比例对合金力学性能的影响[J]. 塑料 2020(05)

- [27].潞宝尼龙6短纤维项目投产[J]. 山西化工 2019(06)

- [28].尼龙水管在新能源汽车上的应用[J]. 汽车实用技术 2020(14)

- [29].油田井下工具尼龙球的高效加工[J]. 西部探矿工程 2019(05)

- [30].国外动态[J]. 塑料工业 2019(11)

本文来源: https://www.lw50.cn/article/f233f0db6b7034cdb34ce499.html