# Brillouin OTDR在混凝土裂缝检测中的应用研究

### 论文摘要

在当今世界建筑结构中,混凝土是运用最广泛、用量最多的建筑材料之一,具有抗压强度较大但抗拉强度很小的特点。一旦混凝土所受的应力超过其极限抗拉强度时,就会出现裂缝,降低混凝土结构的抗渗和抗疲劳等性能,导致水分及有害物质的渗入,加速钢筋的锈蚀和混凝土的自然老化,最终损害结构的使用功能和耐久性,直接危害混凝土工程安全。在大型混凝土结构安全检测中,混凝土裂缝是一项重要的指标。全方位在线监测混凝土裂缝,对预示和征兆混凝土工程中的险情具有重要意义,并根据监测结果进行及时的原因分析和修复,是保障混凝土结构稳定、安全运行的有效措施。本文以玻璃纤维增强塑料(GFRP)单芯应变传感光缆作为Brillouin OTDR分布式传感技术的光信号传输通路和传感器,对混凝土裂缝的测量进行了相关理论分析和实验研究。采用贴附法将GFRP单芯应变传感光缆与纵向钢筋成30°、60°、90°埋设于钢筋混凝土试件的中间部位,在温度和外加应力的作用下,光纤中的背向布里渊散射光频率将产生相应的移位。本文主要研究内容如下：(1)对GFRP单芯应变传感光缆进行了加卸载拉伸实验,获得其应变影响参数为1.04,进行三次水浴法温升实验,获得GFRP单芯应变传感光缆的温度影响参数为0.93。(2)设计了混凝土试件的尺寸和GFRP单芯应变传感光缆在混凝土试件中的布设线路,选择贴附法完成了GFRP单芯应变传感光缆的埋设,建立了分布式监测线路与混凝土试件之间的拓扑关系。(3)对混凝土凝固养护过程中的温度裂缝和凝固后外力作用下的受力裂缝进行了监测。监测结果表明：混凝土试件浇筑完成当天应变呈增大趋势,应变变化量区间为520με～2200με,随着混凝土的逐渐凝固应变趋向稳定。凝固后,外力作用使得应变变化量呈增大趋势,随着裂缝的产生,在光缆433.8 m处达到最大应变变化量2318με。(4)建立了基于Brillouin OTDR的混凝土垫层裂缝监测系统,采用.NET技术设计并开发了混凝土垫层裂缝监测软件,对混凝土垫层裂缝数据进行了分析处理,实现了混凝土垫层裂缝产生前预报裂缝和裂缝产生后监测裂缝的功能。

### 论文目录

- 摘要

- Abstract

- 目录

- 第一章 绪论

- 1.1 引言

- 1.2 混凝土裂缝成因与分类

- 1.2.1 荷载裂缝

- 1.2.2 温度裂缝

- 1.3 典型混凝土裂缝检测方法

- 1.3.1 人工现场测定法

- 1.3.2 点式传感检测法

- 1.3.3 基于OTDR的分布式光纤检测技术

- 1.4 Brillouin OTDR在混凝土裂缝中的应用

- 1.5 小结

- 第二章 基于GFRP单芯应变传感光缆的Brillouin OTDR工作原理与测试

- 2.1 引言

- 2.2 GFRP单芯应变传感光缆的结构与性能

- 2.3 基于GFRP单芯应变传感光缆的Brillouin OTDR工作原理

- 2.4 GFRP单芯应变传感光缆的温度影响参数测量实验

- 2.4.1 温度影响参数测量原理

- 2.4.2 温度影响参数测量过程

- 2.4.3 温度影响参数测量数据分析

- 2.5 GFRP单芯应变传感光缆的应变影响参数测量实验

- 2.5.1 应变影响参数测量原理

- 2.5.2 应变影响参数测量过程

- 2.5.3 应变影响参数测量数据分析

- 2.6 小结

- 第三章 基于Brillouin OTDR的混凝土裂缝监测实验

- 3.1 引言

- 3.2 钢筋笼的扎制

- 3.3 GFRP单芯应变传感光缆的布设

- 3.3.1 GFRP单芯应变传感光缆布设线路设计

- 3.3.2 GFRP单芯应变传感光缆的安装

- 3.3.3 GFRP单芯应变传感光缆的定位

- 3.4 钢筋混凝土试件的浇筑

- 3.5 混凝土的温度裂缝监测

- 3.6 混凝土的应力裂缝监测

- 3.7 小结

- 第四章 Brillouin OTDR在混凝土垫层中的应用

- 4.1 引言

- 4.2 混凝土垫层裂缝监测系统的总体设计

- 4.3 混凝土垫层裂缝监测软件的设计

- 4.4 混凝土垫层裂缝监测数据

- 4.4.1 数据采集

- 4.4.2 数据存储

- 4.5 数据处理与模型分析

- 4.5.1 应变测算

- 4.5.2 测算结果显示

- 4.5.3 距离应变曲线生成

- 4.5.4 裂缝预警

- 4.6 小结

- 第五章 总结与展望

- 5.1 总结

- 5.2 展望

- 致谢

- 参考文献

- 附录A 攻读硕士学位期间发表论文与参加课题

- 附表B 实验数据表

### 相关论文文献

- [1].Stimulated Brillouin scattering by the interaction between different-order optical and acoustical modes in an As_2Se_3 photonic crystal fiber[J]. Chinese Optics Letters 2020(01)

- [2].Brillouin wavelength-selective all-optical polarization conversion[J]. Photonics Research 2020(04)

- [3].Distributed Brillouin frequency shift extraction via a convolutional neural network[J]. Photonics Research 2020(05)

- [4].Velocity and Stability of Condensed Polymorphic SiH_4: A High-Temperature High-Pressure Brillouin Investigation[J]. Chinese Physics Letters 2020(06)

- [5].High-gain and low-distortion Brillouin amplification based on pump multi-frequency intensity modulation[J]. Chinese Physics B 2019(02)

- [6].Visible Raman and Brillouin lasers from a microresonator/ZBLAN-fiber hybrid system[J]. Photonics Research 2019(05)

- [7].A useful method for determination of optimal fiber input power in spontaneous Brillouin-scattering-based sensing system[J]. Optoelectronics Letters 2018(01)

- [8].Impact of Brillouin amplification on the spatial resolution of noise-correlated Brillouin optical reflectometry[J]. Chinese Optics Letters 2017(08)

- [9].Tunable self-seeded multi-wavelength Brillouin-erbium fiber laser based on few-mode fiber filter[J]. Optoelectronics Letters 2017(06)

- [10].Measurement of Brillouin gain coefficient in fluorocarbon liquid[J]. Chinese Optics Letters 2016(04)

- [11].Cooling rate calibration and mapping of ultra-short pulsed laser modifications in fused silica by Raman and Brillouin spectroscopy[J]. International Journal of Extreme Manufacturing 2020(03)

- [12].Stimulated Brillouin scattering induced all-optical modulation in graphene microfiber[J]. Photonics Research 2019(01)

- [13].Bandwidth-reconfigurable single-passband microwave photonic filter based on stimulated Brillouin scattering[J]. Optoelectronics Letters 2019(01)

- [14].Molecular Application of a State Specific Multi-Reference Brillouin-Wigner Perturbation Theory[J]. Chinese Physics Letters 2016(02)

- [15].SNR improvement in self-heterodyne detection Brillouin optical time domain reflectometer using Golay pulse codes[J]. Optoelectronics Letters 2017(06)

- [16].Investigation of combined Brillouin gain and loss in a birefringent fiber with applications in sensing[J]. Chinese Optics Letters 2014(12)

- [17].Demonstration of laser pulse amplification by stimulated Brillouin scattering[J]. High Power Laser Science and Engineering 2014(04)

- [18].Influence of laser linewidth on performance of Brillouin optical time domain reflectometry[J]. Chinese Physics B 2013(07)

- [19].Stimulated Brillouin scattering-induced phase noise in an interferometric fiber sensing system[J]. Chinese Physics B 2012(03)

- [20].Signal Processing for Fibre-optic Distributed Sensing Techniques Employing Brillouin Scattering[J]. Semiconductor Photonics and Technology 2009(01)

- [21].A high-efficiency Brillouin fiber ring laser[J]. Chinese Optics Letters 2009(06)

- [22].Performance Analysis of Temperature and Strain Simultaneous Measurement System Based on Heterodyne Detection of Brillouin Scattering[J]. Journal of Electronic Science and Technology of China 2008(04)

- [23].Theoretical analysis of the relationship between the Brillouin gain coefficient and the strain in the optical-fiber sensors[J]. Optoelectronics Letters 2008(04)

- [24].Brillouin cavity optomechanics sensing with enhanced dynamical backaction[J]. Photonics Research 2019(12)

- [25].Switchable Brillouin frequency multiwavelength and pulsed fiber laser[J]. Chinese Optics Letters 2017(10)

- [26].Improved all-optical OR logic gate based on combined Brillouin gain and loss in an optical fiber[J]. Chinese Optics Letters 2014(08)

- [27].Bursting behaviours in cascaded stimulated Brillouin scattering[J]. Chinese Physics B 2012(01)

- [28].A new method for measuring the threshold of stimulated Brillouin scattering[J]. Chinese Physics B 2012(07)

- [29].Photonic crystal ber-based multi-wavelength Brillouin ber laser with dual-pass ampli cation con guration[J]. Chinese Optics Letters 2011(02)

- [30].Using Brillouin fiber-optic ring laser to provide base station with uplink optical carrier in a 10 GHz radio over fiber system[J]. Journal of Shanghai University(English Edition) 2009(06)

本文来源: https://www.lw50.cn/article/fa869ff106b809680c8eea08.html